## Slide 1
RASPBERRY PI
Under Guidance Of:
Dr. Manju K Chattopadhyay
Presented By:
Ashish Porwal (16MTES03)
Murtaza Ameen (16MTES09)

## Slide 2
Contents:
Introduction to Raspberry Pi.
Communication protocols.
First Time Setup.
Webpage Development.
Introduction to MySQL.
Server and Client application of RPi.
Server Based Robot Using RPi and Android app.
Conclusion

## Slide 3
Introduction:
Lets start Raspberry Pi as just Pi to save some real estate 
“Pi is a single board computer”.
Pi is small scale computer in size little bigger than a credit card.
Developed in United Kingdom by Raspberry Pi foundation.
Pi was introduced as an educational gadget for those who want to learn programing.
Pi is based on Broadcom SoC (System on Chip) with an ARM processor.
Consists a GPU and 1 GB of RAM.
The boot media is a SD card and can also be used for persist data.
Pi can be used as a cheap computer for experiments and education purposes.
Cost of Pi is around Rs. 3000 for a B model.
[1]

## Slide 4
GPIO pins
On board
Bluetooth
Wifi
DSI display port
SD card slot
Micro usb power input
Full size HDMI video port
CSI camera port
3.5mm audio jack
10/100
LAN port
4 USB 2 ports
LAN controller
Broadcom BCM2837 64bit
Quad core CPU at 1.2GHz
1GB RAM
Dimension
85.6mm x 56mm x 21mm

## Slide 5
GPIO pins
Pin Configuration
2- 5v power supply pins.
2- 3.3v power supply pins.
8- Ground pins.
17- General I/O pins.
2- I2C interface pins.
5- SPI interface pins.
2- UART pins.
2- ID EEPROM interface pin.

## Slide 6
Processor
1.2GHz
64-bit
quad-core
ARMv7 CPU
1GB RAM

## Slide 7
DSI (display serial interface)
port

## Slide 8
Small board size: 25mm x 20mm x 9mm.
5MP (2592×1944 pixels) Omni vision 5647 sensor in a fixed focus module.
Support 1080p30, 720p60 and 640x480p60/90 video record.
CSI (camera serial interface)
Port

## Slide 9
HDMI Port
HDMI port is used to connect pi with TV or other HDMI supported devices.
Audio and video both are supported through HDMI port.

## Slide 10
SPI Protocol:
SCLK
MOSI
MISO
SS1
SS2
SS3
SCLK
MOSI
MISO
SS
SCLK
MOSI
MISO
SS
SCLK
MOSI
MISO
SS
SPI
SLAVE 1
SPI
SLAVE 2
SPI
SLAVE 3
SPI
MASTER

## Slide 11
I2C Protocol:
SCL SDA
SCL SDA
SCL SDA
Master
Slave 1
Slave 2

## Slide 12
First Time Setup

## Slide 13
Requirements:
Sd card
HDMI cable
USB keyboard
Micro USB
Raspberry Pi
USB Mouse
LAN cable
Display Device

## Slide 14
Download Raspbian OS:
Open www.raspberrypi.org.
Go to ‘Downloads’ section.
Click on ‘Raspbian’.
Then click ‘Download ZIP’ of
‘RASPBIAN JESSIE WITH PIXEL’
Direct Link for Downloading
Zip file https://downloads.raspberrypi.org/raspbian_latest
It requires 1.5 Gb size in your
computer.
Now extract image file from
Zip file.
The extracted file is about of
size more than 4 Gb.

## Slide 15
Insert micro sd card in computer.
Open SDFormatter software.
Select Full Erase from option menu.
Click on Format button.
Format SD card
Download Link of SDFormatter for windows:
https://www.sdcard.org/downloads/formatter_4/eula_windows/SDFormatterv4.zip

## Slide 16
Install Raspbian OS on micro SD card:
Open Win32DiskImager software
Provide the path of Raspbian Image file
which you already downloaded
Click on ‘Write’ button.
It takes around 10 minutes to install OS.
Now your SD card is ready with Raspbian
OS Loaded in it.

## Slide 17
Let us Start with Pi:
Insert SD card inside your Raspberry pi.
Plug mouse and key board.
Connect RPi with HDMI supported TV or Monitor
Provide 5v power to RPi using micro USB.
Open the RPi terminal and write the command:
Sudo raspi-config
Select option 7 (Advanced Options)
Then select SSH and enable it.

## Slide 18
Provide static IP to RPi:
Open the terminal.
Write command sudo nano /etc/dhcpcd.conf
At the end of file write:
Interface wlan0
Inform 192.168.43.94
Interface eth0
Static ip_address=169.254.187.41
Note: Do not alter the content of the file.

## Slide 19
Install putty in windows:
For running your RPi terminal on windows download putty software.
https://the.earth.li/~sgtatham/putty/latest/x86/putty-0.67-installer.msi
Open the Putty.
write the static IP address of RPi in host name edit text.
Then click on open.
Now you are able to run RPi terminal on your personal computer.
Note: If you are connecting RPi using Ethernet cable then write IP address of eth0, else the IP of wlan0 which provided in dhcpcd.conf file.

## Slide 20
Remote Desktop Setup:
Write the command on RPi
sudo apt-get install xrdp
Open remote desktop type IP address of RPi then click on connect.
New window will pop up which asks for username and password.
Default username and password is:
Username- pi
password- raspberry
Now the desktop of RPi is visible in that window, and You can use your key board mouse of your computer for accessing RPi without physically connecting them.

## Slide 21
Commands for installing important libraries:
Open terminal and write following commands.
Sudo apt-get update
Sudo apt-get install motion
sudo apt-get install apache2
sudo apt-get install php5 libapache2-mod-php5
sudo apt-get install apache2 php5 php5-mysql mysql-server
Sudo apt-get install python3-rpi.gpio

## Slide 22
Developing First webpage:
HTML code:
<!DOCTYPE html>
<html>
<title>SOEX</title>
<body>
<h1>my first page</h1>
<image src=“aaa.jpg”>
<video width="320" height="240" controls> <source src="movie.mp4" type="video/mp4"> not supported. </video>
<audio controls> <source src=“abhiabhi.mp3" type="audio/mp3"> not supported. </audio>
</body>
</html>

## Slide 23
Webpage with javascript:
<!DOCTYPE html>
<html>
<title>SOEX</title>
<body>
<h1 id=“head”>my first page</h1><br>
<h1 id=“head2”>SOEX</h1><br>
<button type=“button” onclick=“changeHeading()”>Click</button>
<button type=“button” onclick=“document.getElementById(“head2”).innerHTML=Date();
”>Click</button>
<script>
function changeHeading(){
document.getElementById(“head”).innerHTML=“hello Engineers”;
}
</script>
</body>
</html>

## Slide 24
<!DOCTYPE html>
<html>
<body>
<form action="" method="POST">
<input type=“text” name=”text”>
<input type="submit" name="form_submit" value=“Enter">
</form>
</body>
</html>
<?php
if(isset($_POST['form_submit']))
{
echo $_POST[‘text’];
}?>
Webpage with PHP

## Slide 25
Introduction to MySQL:
Enter the commands.
mysql –u root -p
Enter MySQL password.
Create database database_name ;
use database_name ;
create table student_info (id int auto_increment primary key, name text) ;
describe student_info ;
insert into student_info (name) value (“Ashish”) ;
insert into student_info (name) value (“Murtaza”) ;
Select * from student_info ;
Delete from student_info where name=“Murtaza” ;

## Slide 26
<!DOCTYPE html>
<html>
<body>
<form method="POST" action="pre8.php">
ENTER YOUR NAME:<input type="text" name="name">
<br>
<input type="submit" value="Send to SERVER">
</form>
</body>
</html>
<?php
$name=$_POST["name"];
$dbms=new mysqli("localhost","root","123","database_name3");
if($dbms->connect_error){
die("Connection Failed!").$dbms->connect_error;
}
else{
if($dbms->query('INSERT INTO student_info(name) value ("$name");')){
echo "Saved";
}
else{
echo "not saved";
}}
?>
Webpage using MySQL:

## Slide 27
SERVER and CLIENT Application

## Slide 28
Sign in Page:
<!DOCTYPE html>
<html>
<body>
<h1>Sign in Page </h1>
<form method="POST" action="abcde.php">
ID:<br>
<input type="text" name="id"><br>
Password:<br>
<input type="text" name="pswd"><br>
<input type="submit" value="Login"><br>
<a href="Log.php">Create new account</a>
</form>
</body>
</html>

## Slide 29
<!DOCTYPE html>
<html>
<body>
<h1>Create new Account </h1>
<form method="POST" action="create.php">
First Name:<br>
<input type="text" name="fn"><br>
Last Name:<br>
<input type="text" name="ln"><br>
DOB:<br>
<input type="date" name="dob"><br>
Password:<br>
<input type="password" name="pswd"><br>
email:<br>
<input type="email" name="ema"><br>
Branch:<br>
<input type="Radio" name="br" value="ES" checked>ES<br>
<input type="Radio" name="br" value="MCT">MCT<br>
<input type="Radio" name="br" value="SIT">SIT<br>
<input type="submit" value="Sign up"><br>
</form>
</body></html>
Sign up Page:

## Slide 30
<!DOCTYPE html>
<html>
<body>
<?php
$name=$_POST["id"];
$pswd=$_POST["pswd"];
$conn=new mysqli("localhost","root","123","ashish");
if($conn->connect_error){
echo "error";
}
else{
if($result=$conn->query("select email,pswd from info;")){
if($result->num_rows > 0){
while($row = $result->fetch_assoc()){
$email=$row["email"];
if($name==$email){
echo "id found ";
if($pswd==$row["pswd"]){
header("Location: profile.php?email=$email");
echo "logged in successfully";
}}}}}}?>
</body></html>
Credentials Verification at SERVER side:

## Slide 31
<!DOCTYPE html>
<?php
if(isset($_FILES['image'])){
$name=$_GET["email"];
$fname=$_FILES['image']['name'];
$fsize=$_FILES['image']['size'];
$ftmp=$_FILES['image']['tmp_name'];
move_uploaded_file($ftmp,"uploads/".$fname);
echo "success";}
if (is_dir("uploads")){
if ($dh = opendir("uploads")){
while (($file = readdir($dh)) !== false){
$auext=array("wav","WAV","mp3","MP3");
$imext=end(explode(".",$file));
$im=array("jpg","jpeg","png","PNG","JPEG","JPG","GIF","gif");
if(in_array($imext,$im)){
echo "<img src='uploads/$file' width='200' height='200'>";
}
if(in_array($ext,$auext)){
echo "<audio controls> \n<source src='uploads/$file' type='audio/mp3'>
\n <source src='uploads/$file' type='audio/wav'>\n </audio>";
}}
closedir($dh);}}
?>

## Slide 32
<html>
<body>
<?php
$email=$_GET["email"];
$conn=new mysqli("localhost","root","123","ashish");
if($conn->connect_error){echo "error";}
else{
$res=$conn->query("select * from info");
if($res->num_rows > 0){
while($row=$res->fetch_assoc())
{
if($email==$row["email"]){
echo "<h1>".$row["name"]."</h1>"."<br>";
echo $row["lastname"];
break;
}}}}
?>
<form action="" method="POST" enctype="multipart/form-data">
<input type="file" name="image"/>
<input type="submit"/>
</form>
</body>
</html>

## Slide 33
SERVER Based Robot using Android App:

## Slide 34
Android App:

## Slide 35
<!DOCTYPE html>
<html>
<body>
<?php
exec("gpio -g mode 4 out");
exec("gpio -g mode 14 out");
exec("gpio -g mode 17 out");
exec("gpio -g mode 18 out");
exec("gpio -g write 4 1");
exec("gpio -g write 14 0");
exec("gpio -g write 17 1");
exec("gpio -g write 18 0");
?>
</body>
</html>
Code section:
Forward:
Reverse:
<!DOCTYPE html>
<html>
<body>
<?php
exec("gpio -g mode 4 out");
exec("gpio -g mode 14 out");
exec("gpio -g mode 17 out");
exec("gpio -g mode 18 out");
exec("gpio -g write 4 0");
exec("gpio -g write 14 1");
exec("gpio -g write 17 0");
exec("gpio -g write 18 1");
?>
</body>
</html>

## Slide 36
<!DOCTYPE html>
<html>
<body>
<?php
exec("gpio -g mode 4 out");
exec("gpio -g mode 14 out");
exec("gpio -g mode 17 out");
exec("gpio -g mode 18 out");
exec("gpio -g write 4 1");
exec("gpio -g write 14 0");
exec("gpio -g write 17 0");
exec("gpio -g write 18 1");
?>
</body>
</html>
Right:
Left:
<!DOCTYPE html>
<html>
<body>
<?php
exec("gpio -g mode 4 out");
exec("gpio -g mode 14 out");
exec("gpio -g mode 17 out");
exec("gpio -g mode 18 out");
exec("gpio -g write 4 0");
exec("gpio -g write 14 1");
exec("gpio -g write 17 1");
exec("gpio -g write 18 0");
?>
</body>
</html>

## Slide 37
Conclusion:
The Raspberry Pi is a powerful little beast and a great platform for building low-cost, but highly capable, embedded systems. The interfaces built into its GPIO connector make it easy to bolt on modules using simple low-cost electronics and a bit of configuration to create very functional and flexible systems. The inclusion of a dedicated camera interface and networking interfaces give you everything.

## Slide 38
?
Query session

## Slide 39
Thank You

## Slide 40
Sudo nano /var/www/html
Run above command on putty or raspbian terminal to access html folder to save ur html php files